## Slide 6
Possible methods of circumventing the 31% efficiency limit for thermalized carriers in a single–band gap absorption threshold solar quantum conversion system.
Intermediate-band solar cell
(B) quantum-well solar cell

## Slide 7
The improvement in efficiency of the cell arises from its potential
(i) to absorb below bandgap energy photons and thus produce additional photocurrent
(ii) to inject this enhanced photocurrent without degrading its output photo-voltage

## Slide 8
Sketch of an intermediate band (IB) solar cell (top) and energy band diagram in thermal equilibrium showing the energy band extremes vs. the depth into the cell (bottom).
Dashed and dotted regions correspond to electron-filled and empty bands respectively (at 0 K)
Role of the two emitters: prevent the IB from contacting the metallic terminals due to metallic character of IB.
IB can be formed by lone pair bands, low dimensionality superlattices, impurities, etc.
Intermediate band (IB) solar cell

## Slide 9
IB is partially filled with electrons --- implies that the Fermi level crosses it.
Under illumination, electrons in the CB are extracted through the n-emitter and holes through the p-emitter.
No carriers are extracted from the IB and hence no transport
(Carriers with high mobility in the IB are not, essential in an ideal device characterized by uniform carrier generation in its bulk [IEEE Trans. Electron Devices 49 (9) (2002) 1632.])
Carrier population in each band is assumed to be governed by quasi-Fermi levels of emitters
The output voltage is determined by the quasi-Fermi level split between the conduction and valence band at the emitter
Output voltage is limited by the total bandgap (εG)
A. Martı´ et al. / Thin Solid Films 511 – 512 (2006) 638– 644

## Slide 10
Efficiency of IB Solar Cells
Type | IB Solar Cell | Single gap SC | Tandem of two SC
Efficiency | 63.2% | 40.7% | 55.4%
Limiting efficiency under maximum solar concentration (46,050 suns)
Optimum gap for IB PV Cell
EH = 1.24 eV
EL = 0.71 eV
A. Martı´ et al. / Thin Solid Films 511 – 512 (2006) 638– 644

## Slide 11
Grown by molecular beam epitaxy (MBE) using the Stranski–Krastanov growth mode.
The barrier and QD materials are GaAs and InAs, respectively.
A silicon delta- (δ-) doped layer, with an areal density approximately to equal the QD density (4x1010 cm-2) is inserted between each QD layer
Confined states are half-filled with electrons via modulation doping.
A. Martı´ et al. / Thin Solid Films 511 – 512 (2006) 638– 644

## Slide 12
IB arises from the confined electron states in an array of quantum dots.
Energy states located within the forbidden bandgap of a conventional semiconductor.
These intermediate levels must behave only as radiative recombination centers.
Quantum Dot Intermediate Band Solar Cell (QD-IBSC)
A. Martı´ et al. / Thin Solid Films 511 – 512 (2006) 638– 644

## Slide 13
Performance of QD IB Solar Cell
Illuminated
Dark
A. Martı´ et al. / Thin Solid Films 511 – 512 (2006) 638– 644

## Slide 14
A. Marti, PRL 97, 247701 (2006)
Intermediate transitions in IB Solar Cell
QD-IBSC sample inside a closed cycle He cryostat
Two optical windows
Halogen lamp – primary light source (filtered by an appropriate set of filters to remove secondary wavelengths)
Primary supplies continuous photons (pumping of electrons from the VB to the IB.)
Role of IR source - illuminate the QD-IBSC with photons of energy below the GaSb bandgap (0.726 eV)  IB to CB
Photocurrent is collected through a low noise and low input impedance current-voltage preamplifier

## Slide 15
Curve 1 (response to primary):
photocurrent produced when pumping with the chopped primary source only (V=1.5 V, T =4.2 K).
Curve 2 (noise background):
photocurrent measured when the IR source is off while the chopper, located in front the of the IR source, is kept spinning (V=0 V, T = 36 K).
Curve 3 (IR on) :
photo-generated current when the IR source is turned on and chopped (V =0 V,
T =36 K).
Intermediate transitions in IB Solar Cell

## Slide 17
, 2) Photogeneration
Collisions and smearing of dist.
Broadening and Thermal equilibrium (Boltzmann Dist.)
Carrier-carrier collisions (uniform dist. of excess energy)
Energy loss by phonon emission (high energy optical and acoustic phonons)
Recombination of electron hole pairs
Loss of excess energy and relaxation to equilibrium states
Hot carrier cells:

## Slide 18
Hot carrier generation
Generation of electron-hole pairs by photons and carrier multiplication by impact ionization
Presence of carrier-carrier scattering and Auger-recombination
Sum of electro-chemical potentials μeh= 0.

## Slide 19
Why do we need a membrane layer?
A hot electron distribution with temperature Teh is only stable, as long as there is no interaction of electrons and holes with phonons.
In the electrodes the interaction with phonons cannot be avoided
Leads to thermalisation from the high carrier temperature Teh to the lattice temperature To
Results in generation of entropy.
Entropy transfers heat to lattice (no longer available for carrier multiplication)
Isentropic cooling

## Slide 20
Isentropic cooling
Avoid energy losses by maintaining carriers with same energy at constant carrier concentrations.
Possible with a narrow band of width dε << kTo
Membrane layer offers states for electrons/holes only in a small energy interval at εe
Typically a large bandgap, small bandwidth material
Cooling, proceeds at constant energy and constant electron concentration and thus at constant entropy in a reversible process.

## Slide 21
εe - Electron energy Δεe - band width in CB εF,e - Fermi level in electron membrane
εh - Hole energy Δεh - band width in VB εF,h - Fermi level in hole membrane
Band diagram of hot carrier cell

## Slide 24
II is an Auger-type process whereby a high energy exciton, created in a semiconductor by absorbing a photon of energy 2Eg, relaxes to the band edge via energy transfer of at least 1Eg to a valence band electron, which is excited above the energy gap [Fig. 1(a)]. The result of this energy transfer process is that two excitons are formed for one absorbed photon. Thus, this process converts more of the high photon energy portion of the solar spectrum into usable energy.

## Slide 26
Active layers comprised of earth-abundant semiconductor absorbers (e.g. Cu2O, Zn3P2, Si, β-FeSi2, BaSi2, Fe2O3) and low-cost plasmonic metals (Al, Cu).

## Slide 27
Plasmonic surface resonance
The excitation of surface plasmons by light is denoted as a surface plasmon resonance (SPR) for planar surfaces
Surface plasmons (SPs), are coherent electron oscillations that exist at the interface between any two materials

## Slide 28
Schematic of a test bed structure consisting of a surface wave interferometer coated with CdSe quantum dots to test plasmonic light absorption. Absorption along the Ag surface is achieved through incident light conversion into surface plasmon polaritons that exhibit mode overlap with the absorber layer.